## Slide 1: Estimating Mineral Weathering Rates in Catskills Watersheds
Chris E. Johnson
Dept. of Civil & Environmental Engineering
Syracuse University

## Slide 2: Erosion, Denudation and Weathering
Erosion: Generally refers to the transport of physical matter by water and wind.
Weathering: Breakdown of rocks/minerals.
  Physical
  Chemical
Denudation: Net lowering of the landscape.
  Result of physical and chemical processes.

## Slide 3: Chemical Weathering
Dissolution of minerals in soils and parent material.
CaAl2Si2O8 (s) + 6H2O + 2H+ = 2Al(OH)3 (s) + Ca2+ + 2H4SiO4 (aq)
Releases dissolved substances to groundwaters.
  Basic Cations: Ca, Mg, K, Na
  Silica: H4SiO4
  Aluminum: potentially toxic to aquatic biota
Neutralizes acidity.
  Crucial to sustainable water quality
  Largely determines “critical load” of acid deposition in forested ecosystems.

## Slide 4: Estimation of Chemical Weathering Rates
Chemical weathering is not readily measurable.
  Very slow rate…
  …integrated over the total mineral surface area in soils and parent material in a watershed…
  …results in relatively large fluxes of Ca, Na, K, Mg, Si, etc.
We need to use indirect methods to estimate fluxes of solutes from chemical weathering.

## Slide 5: Catchment-Based Estimation of Chemical Weathering
Watershed mass balances can be constructed for ions produced by chemical weathering: